## Slide 1: AMI 1.2 Product: Technical Overview
02/24/2016

## Slide 2: Outline
Architecture Overview
AMI 1.2 Features
Power Outage: Detection and Reporting
OTA Protocol: Transport, Reliability, QoS (uStream/MTP)
OTA Meter Program Update
EMCM (AMI Module) FW upgrade
Areas of Concerns
Questions/Answers

## Slide 3: Architecture Overview

## Slide 4: Customer Facing System View
RPMA Total View Appliance or Hosted Service
Network Management Services
Network Controller
Security Management
Services
Network
Database
Services
Ingenu Total View
AMI Protocol &
Device Management
Device Database
Services
Distribution Automation Protocol & Device Management
Digital Oilfield Protocol &
Device Management
SNMP
SNMP
Agent
Communications Controller
Gateway Communications Controller
Ingenu Software
3rd Party Software
Customer Back Office
Data Historian
OMS/
DMS
User Billing
SCADA
CIS
MDMS
EMS
RPMA Access Points
Protocol Adapters (CIM, Multispeak, DNP3)
File Export (CMEP, CSV,…)
REST API

## Slide 5: Service and Endpoint Ecosystems

## Slide 6: Protocol Architecture

## Slide 7: AMI Module (EMCM) FW Architecture

## Slide 8: HES-OTV SW Architecture (AMI only)

## Slide 9: AMI Features

## Slide 10: Design Principles
Good application development practice on RPMA:
  Avoid periodic polling via a downlink (DL) request
  Instead configure device to report periodic data autonomously
    Why?: Since RPMA is designed for high coverage, link is asymmetric: uplink (UL) capacity is much higher than downlink (DL) capacity
  Randomize transmission of periodic data to prevent rx spikes
Over-the-air (OTA) AMI Application Protocol (with exception of non C12.19 complaint I210+) is agnostic to meter platform
  Meter-specific discrimination is done at EMCM that transforms relevant meter data into a unified AMI application protocol
  Rationale: Requires minimum changes on backend SW to bring up new meter platforms

## Slide 11: Feature List
Bootstrapping*: Data Order Configuration Install
Meter Readings:
  Scheduled and on-demand Billing Data Read/Report
  Scheduled and on-demand Load Profile Read/Report
  Scheduled and on-demand “Power Quality” Read/Report
Events:
  EMCM Status Events
  Meter Status Events
  logged Meter Events

## Slide 12: Feature List (continued)
End Device Control
  EMCM Soft/Hard Reset
  Remote Connect/Disconnect
  Load Control
    DLP/ECP/PPM enable/disable (I210+c)
    Load Control Override Disable (SGM3000)
  Demand Reset (Immediate/Scheduled)
  RTP/CPP Enable/Disable
  Season Change
  Clear Meter Flags* (Status Indicators)
Debug/Reconfig*: Available OTA only via HES Debug port:
  EMCM Panic Block Request/Response
  Get and/or update factory installed EMCM configuration

## Slide 13: Data Orders
Data Orders (/opt/onramp_apps/hes/instance_1/data_orders.properties)
  Generic installable configuration for a group of meters
    Meters with same “Data Report Config Name” (OTV: Devices->Properties) are associated with same data order
    If the attribute is not assigned, default data orders for each meterType is used
What can be configured?
  Read/Report Periods of billing data, LP, power quality data
  Poll Periods of meter indications and power quality events
  Filters that can be used to restrict desired quantities
  DST configuration
    Mainly for GE meters in “demand only” mode as they don’t have notion of time
  Additional stuff with defaults in EMCM  not changed for most part!

## Slide 14: Bootstrapping: Data Orders
Installed configuration is dependent on
  Meter metrology configuration (UOMs) retrieved from ST12-16, ST21-22 and ST61-62
    Metrology configuration is reported by EMCM in “MeterConfigReport”. An AES-128 hash over this information (meterDataReportHash) is used to keep HES and EMCM in sync with regards to metrology information
    This makes AMI solution agnostic to changes in meter program as the hash changes lead to boot process whereby HES and EMCM sync up  Design Philosophy 3
  Installed configuration is identified by orderId
    Stored persistently in both HES and EMCM. HES keeps a history of 1
    orderId (32-bit unix timestamp) is included in billing/interval report to uniquely identify configuration.  Avoids periodic tx of config information

## Slide 15: UOM -> CIM
32-bit ANSI UOM: Unit of Measure
  Defined in ANSI C12.19 in ST12
    Called “Measurement Profile” in GE meters and configurable via MeterMate
  A wide universe of possibilities
    That can be further expanded by meter vendor by setting NFS bit!
CIM: Common Information Model
  Ingenu AMI solution complies with IEC-61968-9 edition 1.0
  ReadingType (Annex C) is a 9 digit code
iec-cim-http.properties
  Dictionary file to translate uoms  cims (meter dependent!)
  Eg: meter.model.I210PLUSC.context.tou_summation.uom_hex_code.0x00024000=0.0.9.1.0.12.3.<tier>.0.0.72

## Slide 16: Bootstrapping
Call flow described in AMI HLD
Take away:
  Adapts to meter configuration (program): Metrology configuration change makes EMCM “unauthorized” till it does a successful boot syncs with HES
  Reduced overhead once synced: Post sync, a single BootInd message from EMCM->HES
  Hot swapping: For SGM3000 meters, “Meter Serial Number” reported in BootInd is verified against that reported via marriage file
  EndDeviceInfo is other meter info
    Displayed in OTV under Device-> Properties

## Slide 17: Scheduled Billing Report
Two periodic BillingDataInd possible:
  BillingOrder 1: All billing data in ST 23: Summations/Demands/Coincidents/TOU
    Stored in EMCM’s internal flash before transmission: Expected read period once every 24 hours
    History of 2 reports stored in flash
  BillingOrder 2: Only summations of total tier recorded in ST23
    Read and kept in RAM till enqueued for tx
    Enables frequent reporting: energy only metering
ReportingPeriod:
  Tx is randomized between [0, reportingPeriod]
  Retried readPeriod/reportingPeriod
    Only if not successfully enqueued to transport layer

## Slide 18: Scheduled Load Profile
Similar to scheduled Billing Report
  Metrology configuration is checked for potential change prior to read
Maximum of 4 periodic LoadProfileInd
  Corresponds to 4 LP sets recorded in ST63-67
  Each report has its own reportingPeriod
Reporting Period:
  readPeriod is irrelevant as persistent storage is provided by meter
  Average number of “intervals” per report = reportPeriod/interval[ST61]
  EMCM memory limitation: Maximum of 16 intervals per report

## Slide 19: Scheduled Power Quality Reports
What is power quality report?
  Instantaneous (rms) values of quantities at time of read
  GE meters don’t use ST28, data is available in manufacturing tables
    MT110 in kV2c and MT113 in I210+c and SGM3000
  AMI 1.2 application protocol specifies following “polyphase” quantities as power quality:
    LtoL Voltage Magnitude, LtoN Voltage Magnitude, Current Magnitude, Momentary PF, Average PF, ITHD, VTHD, TDD, Distortion PF, Temperature, Frequency, Active Power, Reactive Power Distortion VA, Apparent VA
    Quantities reported dependent on what the meter records and data order filtering
      Only kV2c 3-phase currently records all quantities
Reported periodically every reportingPeriod
  Not aligned to midnight but randomly in between [0, reportingPeriod)

## Slide 20: On demand Billing Report
On-demand retrieval of data in ST23
Flexible BillingDataReq OTA
  BillingDataOrder can be used to request specific quantities of interest
Via IEC-CIM/UI, 4 options are provided:
  All data as per installed “data orders”
  All summation quantities in total tier
  Only WH summation quantities in total tier
  Only a specific summation in total tier
   (b),(c),(d) are reduced latency options
GetReadings are mapped to OTA request as per iec-cim-http.properties:
0.0.1.0.0.0.0.0.0.0.72=BillingDataReq.summationsFilterMask_*.*.1.*.*.*.*.*.*.*.72.tiersFilter_0x0

## Slide 21: On demand Load Profile Report
To request interval data stored in ST63 (Set 0) to ST67 (Set 3)
  LP set has to specified
  Time range has to specified: Time range can’t exceed 16 intervals
    Otherwise HES rejects the LP request

## Slide 22: On demand Power Quality Report
Reporting instantaneous quantities as per demand
  Data stored in MT110 (kV2c) and MT113 (I210+c/SGM3000)
Flexible PowerQualityReportReq OTA
  Request any subset of quantities protocol defines
Via IEC-CIM/UI, 4 options are provided:
  All quantities recorded by the meter
  Line-side diagnostics
  Instantaneous demand
  Instantaneous Distortion
   What gets reported is decided by iec-cim-http.properties
  eg. 12.0.0.0.0.47.0.0.0.0.0=PowerQualityReportReq.selectFlags_0x21e8.selectFlags2_0x0

## Slide 23: Events
Two main kinds:
  Current Events:
    AppEvents i.e. EMCM events
    Meter Events
      EMCM polls for status indicators recorded by meter. A change in state from previously polled copy in memory is reported
      Poll rate is set by data order (default 5 mins)
      Reported in MeterInd OTA
  Logged Events: Only logged power quantity events are reported
    Events logged with exact timestamp
    Logged events polled at rate set by power quality event reportingPeriod (20 mins) and reported in PowerQualityEventInd

## Slide 24: Current Events
EMCM current events mapped to IEC-CIM:
  Defined in iec-cim-http.properties as AppEvent
Meter Current Events reported in MeterInd:
  RCDC Switch State: ST112
  Generic Meter Status (ST3): stdStatus1 (C12.19), mfgStatus
  Events relating to line-side diag, load control, switch state etc: extraMfg
    MT 72 (I210+c, kV2c) for line-side diagnostics
    MT115 (I210+c) for load control/switch/PPM states
    MT124 (SGM3000) for load control/switch/PPM states
    MT85 (I210+c, kV2c, SGM3000) for RTP/CPP state
    Mapped in iec-cim-http.properties:
    Eg. meter.model.I210PlusC.context.extraMfg.flags.33.set=3.15.16.238.1
    Note: Not all status indicators are mapped in properties file (maybe reported OTA)

## Slide 25: Logged Power Quality Events
Events defined as power quality events in AMI 1.2 protocol:
  Sag/Swell: Logged in MT112 (I210+c, kV2c), MT114 (SGM3000)
  Voltage Imbalance: Logged in MT114 (SGM3000)
  Under Frequency/Over Frequency: Logged in MT114 (SGM3000)
  Momentary Outage: Logged by EMCM in its internal flash after outage detection
    Only details of one momentary outage event is logged, count indicates if multiple events happen between poll
AMI 1.2 application does not retrieve/parse logged events in ST72 periodically

## Slide 26: EndDeviceControl Commands:
Two kinds:
  Immediate
    Executed by EMCM immediately
    All commands
      Connect/Disconnect is immediate only
  Scheduled
    Stored by EMCM in internal flash
    Timer set for execution
    Executed at scheduled time
      RTP/CPP on/off
      Season Change
      Demand Reset
On IEC-CIM, “category type” denotes command

## Slide 27: RCDC
Connect/Disconnect and DisableOverride (SGM only)
TTL of 1 hour is default at HES
  Configurable
  Translated to end time (POSIX) in OTA message
  If requested is received after end time, EMCM drops the request

## Slide 28: Demand Reset
Meter calendar driven demand reset is NOT recommended
  Race condition with EMCM read of ST23 for demand data
Two ways to set Demand Reset:
  Configure via Data Orders:
    Set Daily Demand Reset/Month Demand Reset
    Issue: Utilities don’t use fixed billing periods
  Command EMCM to execute Demand Reset (immediate/scheduled)
    Immediate demand reset is executed immediately
    Scheduled demand reset is executed by EMCM right after billing data read (order 1) if it falls between startTime and endTime of scheduled command
OTV provides a task manager to set DemandResetReq before the end of billing cycle

## Slide 29: Load Control: Meter Differences
In 120+c: Load control points (ECP/DLP/PPM/Lockout) are mapped as auxiliary relays
  Enable/Disable them with RCDC command
    0: Main relay; 1: ECP, 2: DLP; 3: PPM; 4: Lockout
  Required as RCDC command to main relay automatically disables these load control points!
In SGM3000 meters, enabling/disabling of load control points is via meter program
  However RCDC command to main relay temporarily “overrides” other controls
  It is required to “Disable Override”

## Slide 30: Power Outage
Detection and Reporting

## Slide 31: Power Outage Detection and Reporting
Varied Requirements:
  High reliability of reporting sustained outages
    RPMA network star topology provides inherent advantage here
  Eliminate false alarm: reporting momentary as sustained outage
  Low Latency in reporting both outage and outage clear
Approach:
  RPMA Node is put into deep sleep mode via “PowerFailNotification”
  EMCM in low power state monitors PF (and ZC in I210+c, kV2c, COMP1 in SGM) to determine momentary/sustained outage
  PowerFailConfirm wakes node up and it sends short “LastGASP”
  Outage Clear is generated when node attempts to join post power fail
    Reduces latency as establishing data session takes time
  Power fail timestamps also reported in BootInd

## Slide 32: Power Fail Timeline
Power fail/power fail clear indication are sent by node for fast delivery
  Can be leveraged by any application
Momentary vs sustained outage detection and triggering power fail events is done by EMCM

## Slide 33: Momentary vs Sustained Outages
Three parameters:
  maxMomentaryOutageDuration (default 2 min)
  maxMomentaryInteruptionDuration (default 20 sec for I210+c/kV2c, 120 secs for SGMs)
  minPowerOnDuration (default=3000msec)
Stored as EMCM config
  Updateable via OTV (OTA message SetMeterCfg)

## Slide 34: Power Fail Notifications: HES side
HES uses power fail information in BootInd to generate events in case LastGASP was lost
  Use case: statistics

## Slide 35: Message Transfer Protocol (MTP)
(uStream) : Reliable, message-based transport protocol with QoS Support

## Slide 36: AMI 1.2 Message Format
Header indicates version
32-bit CRC that prevents against transmission/reassembly errors
Payload in AMI 1.2 is encoded using google protobuffers
  IDL: ami_ota_inf.proto
  Looks and feels like xml but compressed for transmission over wire
Encoded messages are then sent to MTP (Ustream) transport layer for transmission

## Slide 37: MTP (uStream)
Windowing-transport protocol purpose built over RPMA MAC to provide end-to-end reliable delivery and flow control
Message based: Manages fragmentation and reassembly of messages (upto 7 Mbytes)
Built in QoS support: 16 streams (separate for UL/DL) with streamId=0 being highest priority and 15 being lowest
  0, 14, 15 are reserved and used for uStream control: rest available to application
Well-defined API that can be integrated into application FW and SW
  Integrated into host_cmn sw library for device-side
  A standalone java implementation for network side integrated into HES
Provides reliability over both unicast and multicast downlink transports

## Slide 38: Protocol Stack and Buffer Management
Transport Buffer size=8 segments
  Max size of each segment=464byes
USPBuf (EMCM side):
  Common buffer management between application and uStream for transmit side
  Cyclic buffer of size ~ 7680 bytes
    Stream dependent data size reductions can be imposed
  Can hold up to 16 messages (descriptors)
Network side:
  MTP library holds upto 1 message/stream after transport buffer is full

## Slide 39: QoS in AMI via MTP
UL non-resumable streams used: 3, 5, 7, 8
  Highest priority stream 3 reserved for bootstrapping messages and responses to requests: Latency considerations
  Stream 5 for billing data, 7 for other data, 8 for EMCM diagnostic data
  Buffer and descriptor limitations imposed on lower priority streams to prevent lower priority data flood from starving higher priority data
DL non-resumable streams used: 3, 5
  Bootstrapping messages (HES generated) on stream 3
  Data messages on stream 5
Note: Non-resumability => queued data is lost on EMCM reboot

## Slide 40: Resumability
Resumability => Reliable delivery across device reboots (power outage or otherwise)
  Important for delivery of large messages
  Streams can be marked resumable
  Device Application SHALL provide persistent storage for resumable stream state as well as data
In EMCM
  Resumable state is in external flash
  Managed by Data Object Manager (DOM)

## Slide 41: Resumable streams on AMI
Downlink (DL: HES  EMCM)
  Meter Read/Program Update Request : DL Stream 10
    OTA message: C1219Req
    Maximum reserved space in external flash ~50kbytes
    Lowest priority (doesn’t choke other UL messages)
Uplink (UL: EMCM  HES)
  Meter Read/Program Update Response: UL Stream 10
    OTA message: C1219Rsp
    Maximum reserved space in external flash ~50kbytes
    Lowest priority (doesn’t choke other UL messages)
Future uses: Meter FW upgrade, (EMCM FW upgrade)

## Slide 42: Reliable Multicast
RPMA system provides multicast user data (MUD) channel for transport of DL data
  Useful for transmitting same request to large number of devices
  Group management is done by RPMA GW
  MUD on RPMA network is best effort!
Ustream provides a wrapper that enables reliable multicast
  Internally Ustream uses MUD channel, collects feedback and lost fragments are transmitted over reliable unicast
    Greatly simplifies application development
  Application has to create and manage MUD groups
    Ustream API expect groupId and members of groups to be provided

## Slide 43: Reliable Multicast
Reliable multicast is used by AMI mainly for sending “Meter Program Update”

## Slide 44: Meter Read/Program Update
C1219Req/C1219Rsp

## Slide 45: C1219Req/Rsp
AMI protocol message that specifies sequential C12.18 (PSEM) operations to read/modify meter data stored in ANSI C12.19 data format in single C12.18 session
  C12.18 Actions: READ/WRITE/PROCEDURE
  EMCM Actions: PATCH/DELAY/(READ&COMPARE)
  Number of retries can be specified (fixed in HES to 3)
C1219Rsp: Returns read data and result of operation
  Various verbosity levels
Use cases:
  Meter Program (Configuration) Update
  Large table reads for debug/audit purposes

## Slide 46: Program Update: Procedure
GenericSchema.xsd
  Program.xml should validate against this schema
  Features:
    Compatibility check: Meter Model, FW version, ElementVolts etc
    Programming: Set of instructions that programs the meter
    Audit Check: Validate that changes took place
  Note: This schema was basis of proxml conversion in MeterMate 6.4 and 6.5. Ingenu has tested program update only against MeterMate 6.4 generation
  Alcara (formerly GE) has notified that recently released MeterMate 6.6 has new version of program.xml based on modified schema.
    OTV 1.2 is not compatible with new schema
    Feasible C1219Req as defined doesn’t need modification
HES: Program.xml  C1219Req for OTA tx

## Slide 47: Some other tidbits…
C1219Req/Rsp are mapped to resumable streams
  Stream 10 on DL (Req) and stream 10 on UL (Rsp)
Ustream protocol limits 1 message per resumable stream
  Memory requirements otherwise are high!
  This implies that when sending a C1219Req to a group, none of the devices should have a pending unacknowledged C1219Req
    One member of the group can hold the entire group!
    “Flush” terminates any unfinished messages on a stream and clean up states
    Allows new requests to be enqueued
“Abort Meter Operation”C1219AbortReq
  Aborts execution of request and if done aborts tx of C1219Rsp

## Slide 48: EMCM Processing of C1219Req Fragments

## Slide 49: EMCM FW Update

## Slide 50: EMCM FW Update
Managed in AMI 1.2 via EMS
  Same code download broadcast protocol that is used for RPMA node FW update
  Reason: Have had years of test coverage and field use
  Limited to < 250 kbytes download (RPMA node flash limitation)
  Transferred to EMCM’s external flash for staging: Managed by DOM (data object manager)

## Slide 51: BACK UP

## Slide 52: MPU: HES state transitions

## Slide 53: MPU: EMCM State Transitions

## Slide 54: I210+c ECP/DLP state transition (relevant for Haseko)

## Slide 55: Outstanding Areas of Concern
HES/EMCM/Meter

## Slide 56: Program Update: Known Issues I
Program.xml generated by MeterMate 6.4 (and for partly tested 6.5) is insufficient and have lot of errors
  Insufficient as there is no way to compare bitfields (< 8 bits)
    Work around: Remove from Compatibility test (Element Volts)
      Remove ElementVolts, no softswitch check etc: should be managed via OTV group creation feature so that invalid program doesn’t reach a meter
  Errors
    Work around: Ingenu maintains a list (MM 6.4 only!) and hand edits program.xml
    Alcara has introduced new errors in program.xml generation in MM 6.5
Meter program clears all meter data
  Work around:
    Remove SP3 (clear meter data procedure) from program.xml (occurs twice)
    Ensure that ST12-15 writes are removed and instead

## Slide 57: Program Update: Known Issues II
SGM3000 full program update with clear meter data doesn’t work: Not supported
  SGM reboots and breaks C12.18 session in the meter
  C1219Req is designed for update within single C12.18 session
  Work around:
    Most field scenarios require no clearing of meter data.
    Thankfully removing SP3 makes it work!
C12.18 negotiation is not followed on I210+c
  EMCM restarts C12.18 session with parameters acceptable to I210+c

## Slide 58: Other Issues I
Many areas are covered in “Product Requirements Document” for AMI 1.3 and OTV 1.3
HES Horizontal Scalability
Known Ustream issues
  Rare: May happen if mySQL updates are lost: Ustream may get stuck if states are out of sync
    Short term fix: Force Ustream SYNC when detected
    Ustream provides an API to force SYNC: Not exists on OTV UI yet.
  Have been fixed and tested: not ported to released EMCM
Back-to-back DL requests (arriving simultaneously at EMCM) may get overwritten

## Slide 59: Other Issues II
Load Profile data may get time shifted by an hour around DST for the LP block since end block reading timestamp changes
  Note: Separate issue exists with SGM3000 meters: With LP outage recovery enabled and meters without battery causes SGM meters to incorrect report the time associated with reading